## Slide 1
Router Security
The majority of the routers are deployed at the perimeter of the network. Therefore, they are the first line of defense of the network.
Compromise of a router can lead to many issues on the network, such as degrading network performance, denial of network services, exposure of network configuration details and exposure of the sensitive data.
A poorly configured router can easily become compromised

## Slide 2
Router Security
The following section will focus on the “best practice” on how to configure a network router to avoid or prevent very serious security problems.

## Slide 3
Router Security
Physical security is always on top of the list of any best security practice. Routers should be placed in a secure area where it is accessible only to authorized personnel.
The operating system of the router is another crucial component that any network administrator must keep up to date. Most network administrators will settle for the latest stable release of the IOS, but not the very latest one.

## Slide 4
Router Access
Local access and remote access to the router are the common ways of gaining control of a router and access must be restricted only to only authorized personnel.
A typical way of securing the local access or remote access is to create a password.
There are two types of passwords used on a router: the line password and EXEC password.

## Slide 5
Router Access
The line password is used to gain access to the router and the privileged EXEC level password that is used to gain access to EXEC commands.
The line password is recommended to be used in conjunction with the command service-password encryption.
The EXEC level password is enabled with the enable secret password command.

## Slide 6
Router Access
A security step beyond typical password protection is to create a user account for authorized personnel. This provides the capability to track and log each time a system is accessed.
A local user account can be created on a router by using the command username [name] privilege [level] password [password_string] as shown.
RouterA(config)# username admin privilege 10 password @dm1np@$$wd

## Slide 7
Cisco offers AAA (Authentication, Authorization, and Accounting) service as a way to centrally manage and control user access.
With AAA, two of the most used access protocols, RADIUS (Remote Authentication Dial In User Service) and TACACS+ (Terminal Access Controller Access-Control System Plus), are supported.
The following shows an example of how to configure AAA on a Cisco router.
RouterA(config)# aaa new-model
RouterA(config)# aaa authentication login default local group tacacs+
RouterA(config)# aaa authorization exec default local group tacacs+ if-authenticated

## Slide 8
Once the authentication method is defined, it can be applied to any access entry point whether it is local or remote.
The following example shows how to configure a console port with security access. It enforces the authentication using the local user database and the timeout of 5 minutes if the user input is not detected.
Also, it prevents the remote access to the console port via reverse-Telnet with the command transport input none.
RouterA(config)#line con 0
RouterA(config-line)#login local
RouterA(config-line)#exec-time 5 0
RouterA(config-line)#transport input none

## Slide 9
Remote Access
The remote access to the router can be made via Telnet or SSH. Telnet is a default transport protocol into a router, but its unencrypted traffic is a big security flaw.
Therefore, SSH is recommended whenever possible. To enable the SSH transport requires an extra step of generating an RSA key.
To generate the key, the command crypto key generate rsa is issued.
RouterA(config)#crypto key generate rsa

## Slide 10
RSA Key
After the RSA key is generated, the remote VTY access can be configured with SSH as the transport.
RouterA(config)# line vty 0 4
RouterA(config-line)# access-class 15 in
RouterA(config-line)# login authentication default
RouterA(config-line)# transport input ssh
RouterA(config-line)#exec-time 5 0
The command transport input ssh enforces SSH as the only access method.

## Slide 11
RSA Key
After the RSA key is generated, the remote VTY access can be configured with SSH as the transport.
RouterA(config)# line vty 0 4
RouterA(config-line)# access-class 15 in
RouterA(config-line)# login authentication default
RouterA(config-line)# transport input ssh
RouterA(config-line)#exec-time 5 0
The access-class 15 defines the access list of the network that is allowed to connect to the router via SSH.

## Slide 12
RSA Key
After the RSA key is generated, the remote VTY access can be configured with SSH as the transport.
RouterA(config)# line vty 0 4
RouterA(config-line)# access-class 15 in
RouterA(config-line)# login authentication default
RouterA(config-line)# transport input ssh
RouterA(config-line)#exec-time 5 0
Lastly, the exec-timeout of 5 minutes is configured.

## Slide 13
Router Services
A router has many services enabled by default. Unnecessary services should be disabled and those services deemed necessary should be tightened.
The TCP/IP services like echo, discard, daytime, chargen, bootps, finger, identd, and snmp, are enabled automatically on a Cisco router and most of these are not needed. They can be disabled globally as shown below:
RouterA(config)#no service tcp-small-servers
RouterA(config)#no service udp-small-servers
RouterA(config)#no ip bootp server
RouterA(config)#no service finger
RouterA(config)#no ip identd

## Slide 14
Router Services
The newer Cisco IOS supports web-based remote administration; however, HTTP has no encryption.
Therefore, web-based administration via HTTP can reveal the passwords and should be avoided.
More recent Cisco IOS releases do provide another option of HTTPS that provides end-to-end SSL encryption as shown:
RouterA(config)# no ip http server
RouterA(config)# ip http secure-server
RouterA(config)# ip http access-class 15
RouterA(config)# ip http authentication aaa

## Slide 15
Router Services
It is highly recommended that services such as CDP, remote configuration downloading, and source-routing are disabled as shown.
RouterA(config)#no cdp run
RouterA(config)#no service config
RouterA(config)#no ip source-route

## Slide 16
Router Services
On the interface level, any unused interfaces should be disabled, so that they cannot participate in any network activity.
Directed broadcasts allow a host on another network segment to initiate a broadcast to a different network segment and this can be used as a denial of service attack like the smurf attack.
The directed broadcast feature should be disabled. Newer IOS versions disable the directed broadcast by default.

## Slide 17
Router Services
The router interfaces should not be acting as the intermediary for ARP or ARP proxy.
The following is the example configuration to secure the router interface.
RouterA(config)# interface fastethernet0/1
RouterA(config-if)#shutdown
RouterA(config)# interface fastethernet0/2
RouterA(config-if)# no ip directed-broadcast
RouterA(config-if)# no ip proxy-arp
RouterA(config-if)# no ip unreachables
RouterA(config-if)# no ip redirects
RouterA(config-if)# no ip mask-reply

## Slide 18
Router Logging
Logging allows the administrator to analyze the events that occur and use the given information to correlate and find the issues.
It is recommended that for best security, syslog logging and buffered logging in debugging level should be set up.
To keep accurate logs, the correct time on a router has to be set up. This tends to be a step that many disregard. Cisco routers support the Network Time Protocol (NTP), which can be set up to synchronize the router’s clock with the time server.

## Slide 19
Router Logging
The following example shows the log configuration of a Cisco router. It consists of enabling timestamp service for log with the date and time down to millisecond detail.
RouterA(config)# service timestamps log datetime msec
RouterA(config)# logging on
RouterA(config)# logging buffered 16000 debugging
RouterA(config)# logging trap debugging
RouterA(config)# logging 172.20.20.20
The logging is enabled by the command logging on

## Slide 20
Router Logging
The following example shows the log configuration of a Cisco router. It consists of enabling timestamp service for log with the date and time down to millisecond detail.
RouterA(config)# service timestamps log datetime msec
RouterA(config)# logging on
RouterA(config)# logging buffered 16000 debugging
RouterA(config)# logging trap debugging
RouterA(config)# logging 172.20.20.20
A memory buffer of 16Kbytes was reserved for logging with debugging level.

## Slide 21
Router Logging
The following example shows the log configuration of a Cisco router. It consists of enabling timestamp service for log with the date and time down to millisecond detail.
RouterA(config)# service timestamps log datetime msec
RouterA(config)# logging on
RouterA(config)# logging buffered 16000 debugging
RouterA(config)# logging trap debugging
RouterA(config)# logging 172.20.20.20
In addition, the same debugging level log messages will be sent to a syslog server with the IP 172.20.20.20.

## Slide 22
Access List
Another way to utilize the log is via the access list. As a matter of fact, it is a best practice to use log in every deny statement in each extended access list.
This will provide valuable information of what is being denied and it is very useful as a security detection tool of probes and attacks against the network.
The following is an access list statement with a keyword log :
access-list 101 permit ip 192.168.0.0 0.0.255.255 any
access-list 101 permit tcp any any eq 80
access-list 101 deny ip any any log

## Slide 23
Access List
There is a basic access list that is recommended for every network. This access list is used to protect against IP address spoofing.
The IP address spoof protection concept is very simple; Do not allow any inbound IP packets that contain IP source addresses of the internal network or any reserved private IP addresses.

## Slide 24
Access List
The example shows an access-list 102 that contains a IP address spoofing protection for the internal network of 12.12.12.0/24.
This access list will be applied to the outbound interface of the router as ip access-group 102 in.
access-list 102 deny ip 12.12.12.0 0.0.0.255 any log
access-list 102 deny ip 10.0.0.0 0.255.255.255 any log
access-list 102 deny ip 172.16.0.0 0.15.255.255 any log
access-list 102 deny ip 192.168.0.0 0.0.255.255 any log
access-list 102 permit ip any any

## Slide 25
Switch Security
All discussed security steps or best practices, such as physical security, IOS updates, configuration hardening for local and remote access, disabling unnecessary services, logging and access lists apply to the switches as well.
Switch interfaces or ports directly connect users or network equipment, they should be securely configured to prevent malicious attacks or exploitations from end users.
The very fundamental security rule is to disable the ports that are not being used.

## Slide 26
Switch Ports
A very useful command to use when applying the same command to a group of switch port is the range command.
This makes it easier for the administrator to apply the same security policy on switch ports.
The following example shows the commands to shut down a group or a range of interfaces.
SwitchA(config)# interface range Gigabitethernet1/1-24
SwitchA(config-if)#shutdown

## Slide 27
Switch Port Security
Switch port security can be configured to restrict a port’s ingress traffic by limiting the MAC addresses that are allowed to send traffic into the port.
The command to enable the port security is switchport port-security and this command has to be issued at the interface level.
A switch port can be configured to restrict access by setting a maximum number of MAC addresses or it can be configured to allow only known MAC addresses to pass traffic.

## Slide 28
Along with the security configuration, one will need to define a violation action.
When a violation occurs, one of the selected violation actions will take an effect.
protected, restrict, and shutdown.
protected will drop packets from the violated MAC address(es).
restrict is the same as the protected mode, but it will also send SNMP trap messages to the SNMP server.
shutdown is to shutdown the port and put the port in ERRDISABLE state.

## Slide 29
The following is an example of a port security configuration. This port security is configured to allow only a maximum of two MAC addresses per port and their associated MAC addresses.
If the violation occurs, the switch port will be shut down.
SwitchA(config)# interface Gigabitethernet1/10
SwitchA(config-if)#switchport port-secuirty maximum 2
SwitchA(config-if)#switchport port-secuirty mac-address sticky 0011.2233.440a
SwitchA(config-if)#switchport port-secuirty mac-address sticky 0011.2233.440b
SwitchA(config-if)#switchport port-secuirty violation shutdown

## Slide 30
When a port is in the ERRDISABLE state, an the port is automatically disabled by the switch operating system software because an error condition has been encountered on the port.
This requires a manual intervention by the administrator in order to re-enable the port.
The administrator will need to issue the command shutdown and then no shutdown to re-enable the port.

## Slide 31
Another way of re-enabling a port from ERRDISABLE state is to configure the errdisable recovery feature.
The following example shows the errdisable discovery configuration to recover the port from port security violation after 10 minutes (600 seconds).
SwitchA(config)# errdisable recovery cause psecure-violation
SwitchA(config-if)#errdisable recovery interval 600

## Slide 32
Storm Control
Storm control feature can be used to limit the amount of unicast, multicast, or broadcast packets that each port can receive. When there is an excessive amount of any
The storm can be suppressed by defining the bandwidth percentage of the interface or by defining the bps (bits per second) to limit the bandwidth the unicast traffic is allowed to consume.

## Slide 33
Storm Control
The storm can also be suppressed by defining the pps (packet per second) to limit the number of unicast packets a switch port can forward.
SwitchA(config-if)#storm-control unicast level ?
<0.00 - 100.00> Enter rising threshold
bps Enter suppression level in bits per second
pps Enter suppression level in packets per second

## Slide 34
The storm control is configured with a rising threshold and a failing threshold.
When the traffic rises above the rising threshold, the interface drops that specific traffic until the traffic comes down below the failing threshold.
The administrator can enforce all type of storm controls as shown as the configuration of interface Gigabit Ethernet 1/0/8 in the next slide.

## Slide 35
interface GigabitEthernet1/0/8
storm-control broadcast level 2 1
storm-control multicast level bps 50m 10m
storm-control unicast level pps 6k 2k
storm-control action trap
In this example configuration the broadcast traffic is discarded if it uses more than 2% of the available bandwidth.
This is 20Mbps (2) for a Gigabit interface and it will resume the broadcast traffic again if the traffic falls below 10Mbps (1).

## Slide 36
interface GigabitEthernet1/0/8
storm-control broadcast level 2 1
storm-control multicast level bps 50m 10m
storm-control unicast level pps 6k 2k
storm-control action trap
The multicast storm is set to use only 50Mbps (50m) and its threshold is set at 10Mbps (10m).

## Slide 37
interface GigabitEthernet1/0/8
storm-control broadcast level 2 1
storm-control multicast level bps 50m 10m
storm-control unicast level pps 6k 2k
storm-control action trap
The unicast storm is configured to discard any unicast packets above 6000 (6k) packets per second, the unicast traffic will resume it falls below the 2000 (2k) packets per second.

## Slide 38
interface GigabitEthernet1/0/8
storm-control broadcast level 2 1
storm-control multicast level bps 50m 10m
storm-control unicast level pps 6k 2k
storm-control action trap
The default action for storm-control is to drop packets (trap) when the rising threshold is met.
It can also be configured to shutdown an interface or to send SNMP trap messages.

## Slide 39
Spanning Tree Protocol
STP is a Layer 2 protocol designed to prevent loops within switched networks.
STP builds its topology based on BPDU (Bridge Protocol Data Unit) messages.
A vulnerability associated with STP is that a STP enabled device within the network can actively change the STP topology by sending an unexpected BPDU message.
In order to prevent such events, features such as BPDU guard and BPDU filter can be used.

## Slide 40
Spanning Tree Protocol
On STP enabled switches, a switch port has to go through 4 STP states, (block, listen, learn, and forward) before it can pass traffic.
This process can take between 30 to 50 seconds.
To reduce this time, a switch port can be configured to be an STP Portfast, which speeds up the STP process, and transitions the port into a forwarding state bypassing the listen and learn state.

## Slide 41
STP Portfast
An STP Portfast interface is used to directly connect a host device, which do not send BPDU messages.
BPDU guard is used to prevent a STP Portfast to receive any BPDU message to modify the Spanning Tree topology.
Upon receipt of a BPDU, BPDU guard puts the interface configured for STP Portfast into the ERRDISABLE state.

## Slide 42
STP Portfast
By default, BPDU guard is disabled. The following command is used to globally enable BPDU guard on a Cisco switch.
SwitchA(config)# spanning-tree portfast bpduguard default

## Slide 43
BPDU Filter
The BPDU filter feature effectively disables STP on the selected ports by preventing them from sending or receiving any BPDU messages.
The switch port will ignore all BPDUs received and it will send no BPDUs.
Similar to BPDU guard, the BPDU filer can be configured globally or on an individual port.
The global command is spanning-tree portfast bpdufilter default.
The command to enable the BPDU filter on the interface level is spanning-tree bpdufilter enable.

## Slide 44
STP Root Guard
STP Root guard allows participation in spanning tree and BPDU messages as long as the attached device does not attempt to become the root bridge.
Essentially, STP Root guard provides a way to enforce the root bridge placement in the network.
If an unauthorized device starts sending BPDU messages with a better bridge ID, the Root guard disables the switch port on which those BPDU messages were received.

## Slide 45
STP Root Guard
The STP Root guard feature can only be enabled at the interface level.
It is recommended to apply this feature to those switch ports that are not connected to the root bridge.
The following is the command used within the interface configuration mode to enable STP Root guard.
SwitchA(config-if)# spanning-tree guard root

## Slide 46
VTP (Virtual Trunking Protocol)
Cisco switches come with VTP enabled by default and they are enabled as VTP server mode.
It is possible for a single switch to overwrite all VLAN assignments. It is recommended that VTP be disabled if it is not being used. The following is the example.
SwitchA(config)# no vtp mode
SwitchA(config)# no vtp password
SwitchA(config)# no vtp pruning

## Slide 47
DTP (Dynamic Trunking Protocol)
Dynamic Trunking Protocol is used to automatically negotiate a switch port to be either an access port or a trunk port.
This is convenient, but at the same time can be exploited to reveal all the VLANs or to gain access to all the VLANs.
It is recommended that access ports and trunk ports should all be manually configured without negotiation.

## Slide 48
DTP (Dynamic Trunking Protocol)
Also, it is best practice to control the number of VLANs that are allowed through the trunk port as shown in the example below.
In this example, VLANs 2,3, and 30 are being allowed.
SwitchA(config)# interface gigabitethernet 0/1
SwitchA(config-if)# switchport mode trunk
SwitchA(config-if)# switchport trunk allowed vlan 2,3,30
SwitchA(config-if)# switchport nonnegotiate